| Central Fab Group - Compound Semiconductor | Safety Regulations for Compound Semiconductor Laboratories. |
| --- | --- |
| Approved eye protection must be worn at all times when working in Compound Semiconductor Laboratories. A full face visor must be worn when working at the chemical fumehoods. Hotplates must be attended while on. No wet chemical processing to be done solo outside normal hours. No chemicals are to be left in beakers overnight. Last person leaving the laboratory is responsible for leaving the laboratory in a safe state. (See checklists at the doors – TYNDALL-035F4). Gloves and respiratory protection must be used when handling GaAs dust. New work with hazardous chemicals and other clearly hazardous experiments to be cleared with the Manager of the Compound Semiconductor Fabrication Laboratory before chemicals or equipment are requisitioned. All flammable and toxic gases to be kept in extracted gas cabinets. All new hazardous chemicals to be cleared with Lab manager before they can be used. Breaking of toxic substrates, i.e. GaAs, to be done in designated filtered extract cabinet only. Disposal: a) solvents in disposal cans b) semiconductor materials in the III-V waste container c) waste oil in waste oil drums d) electroplating solutions in waste containers e) acids and alkalis diluted 1000X through sink. Spill Response Actions: a) warn senior personnel within the laboratory and notify the lab manager b) evacuate laboratory and prevent re-entry (if necessary) c) call emergency response group (if necessary) High Voltage (V>400 Volts). All exposed high voltage components must be inside an interlocked enclosure. |